## Slide 1: Quark TCP over RDMA POC
Yulin and Qingming

## Slide 2: Benchmark Configure
CPU: Intel(R) Xeon(R) CPU E5-1630 v4 @ 3.70GHz * 8 core
RDMA NIC: 40GbE Mellanox CX4131A
Switch: Dell S6000 40GbE Switch
MTU 4096 (default 1500)

## Slide 3: Redis Ping
Chart: Throughput(rps, 1t)
| Ping-Inline | Ping-Bulk
RunC | 13175.23 | 13089
Quark | 31746.03 | 34722.22
Chart: Latency(ms)
| PI-P99 | PB-P99 | PI-avg | PB-avg
RunC | 0.127 | 0.111 | 0.067 | 0.067
Quark | 0.031 | 0.031 | 0.014 | 0.013
Chart: Throughput(rps, 50t)
| Ping-Inline | Ping-Bulk
RunC | 70472.16 | 73909.83
Quark | 69686.41 | 71073.21
Chart: Latency(ms)
| PI-P99 | PB-P99 | PI-avg | PB-avg
RunC | 1.015 | 0.903 | 0.424 | 0.405
Quark | 0.503 | 0.479 | 0.368 | 0.372
Quark/RunC | 1 thread | 50 thread
PI-RPS | 2.41 | 0.99
PB-RPS | 2.65 | 0.96
PI-P99lat | 0.24 | 0.50
PI-avglat | 0.21 | 0.87
PB-P99lat | 0.30 | 0.53
PB-avglat | 0.19 | 0.92

## Slide 4: PingPong(request/response)
Chart: Throughput(krps, 1 thread)
| 8 | 128 | 1024
RunC | 19.375 | 1.7695 | 1.6733
BareMetal | 31.25 | 2.8242 | 2.7104
Quark | 101.875 | 9.9648 | 9.0757
Chart: Latency (μs)
| 8 | 128 | 1024
RunC | 51.6 | 56.52 | 59.76
BareMetal | 32.28 | 34.22 | 36.9
Quark | 10 | 10.04 | 11.02
Chart: Throughput(krps, 32 thread)
| 8 | 128 | 1024
RunC | 266.875 | 25.6836 | 26.9053
BareMetal | 359.375 | 36.6758 | 32.9561
Quark | 370.625 | 40.1016 | 31.6821
rps/RunC | 8-1 | 128-1 | 1024-1 | 8-32 | 128-32 | 1024-32
BareMetal | 1.61 | 1.60 | 1.68 | 1.35 | 1.43 | 1.22
Quark | 5.16 | 5.59 | 5.59 | 1.39 | 1.56 | 1.18
Latency/RunC | 8 | 128 | 1024
BareMetal | 0.63 | 0.61 | 0.60
Quark | 0.19 | 0.18 | 0.19

## Slide 5: Known issues Future work
Performance degrade with more TCP connections
Longer connection time
Gap with line speed:
  With bigger payload, Quark can achieve 37.4Gbps which has a small gap (around 1.6 Gbps) compare with raw RDMA and TCP
 | TCP Connection time(μs)
BareMetal | 302
RunC | 355
Quark | 5040
Expected | 10
Share QPs across TCP connections to improve scalability
Pre create QPs to decrease connection time